## Slide 1
INTEGRATED HYDROLOGICAL MODELLING
MIKE SHE
A fully integrated, physically-based framework for modelling
the complete land phase of the hydrological cycle
Components · Interactions · Inputs & Outputs · Academic Applications

## Slide 2
INTRODUCTION
02
2 / 9
What is MIKE SHE?
MIKE SHE is a fully distributed, physically-based hydrological modelling system developed by DHI. Originating from the Système Hydrologique Européen (SHE), it simulates the entire land-based water cycle — from precipitation and evapotranspiration through surface runoff, unsaturated flow and groundwater to river interactions — within a single, tightly coupled framework.
Physically-based
Solves governing equations (Richards, Darcy, Saint-Venant) rather than relying solely on empirical relationships.
Fully distributed
Represents spatial variability across a grid; every cell can have unique soil, land-use and climate properties.
Modular & flexible
Users choose process complexity (simple water-balance to full 3-D) according to data availability and study goals.

## Slide 3
MODEL STRUCTURE
03
3 / 9
Core Process Components
Six process-oriented modules coordinated by a central FRAME component that manages time-stepping and data exchange.
ET
Evapotranspiration
Interception, canopy & soil evaporation, plant transpiration (Kristensen–Jensen or simplified two-layer).
OC
Overland & Channel
2-D overland flow (diffusive wave) + 1-D channel / river network (MIKE 1D).
UZ
Unsaturated Zone
Vertical infiltration & soil moisture (Richards equation, gravity flow or two-layer water balance).
SZ
Saturated Zone
3-D or 2-D groundwater flow using Darcy’s law; multi-layer aquifers.
SM
Snow Melt
Degree-day or energy-balance snow accumulation and melt processes.
EX
Exchange
Dynamic exchange between aquifers and river systems (baseflow, bank storage).

## Slide 4
PROCESS LINKAGES
04
4 / 9
How the Components Interact
MIKE SHE is fully coupled: water and energy fluxes are exchanged at every time step between neighbouring processes. The FRAME component synchronises the different spatial and temporal scales.
Precipitation / Climate → ET + SM + OC
Rain and snow drive the system; intercepted water evaporates or reaches the ground.
Overland Flow (OC) → UZ + Rivers
Ponded water infiltrates into the soil or flows into channels.
Unsaturated Zone (UZ) → SZ + ET
Percolation recharges the groundwater; roots extract water for transpiration.
Saturated Zone (SZ) → Rivers (EX)
Baseflow and bank storage exchange maintain river levels and aquifer heads.
Channel Network → Floodplains / OC
River stages control overbank flooding and return flow to the land surface.
Vegetation / Land Use → ET + Infiltration
Leaf-area index and root depth control evaporative demand and soil moisture dynamics.

## Slide 5
DATA REQUIREMENTS
05
5 / 9
Key Model Inputs
Climate Drivers
• Precipitation (station, radar or gridded)
• Reference ET or radiation, temperature, humidity, wind
• Snow parameters (if relevant)
Surface Properties
• Digital Elevation Model (DEM)
• Land-use / land-cover maps
• Vegetation parameters (LAI, root depth, crop coefficients)
Soil & Subsurface
• Soil hydraulic properties (Ksat, retention curves)
• Geological layers & aquifer parameters
• Specific yield, storage coefficient
River & Boundaries
• River network geometry & cross-sections
• Structures (weirs, gates, pumps)
• Boundary & initial conditions (heads, stages)

## Slide 6
RESULTS
06
6 / 9
Outputs and How They Are Generated
How Output Is Produced
1
Numerical Solution
Each process module solves its governing PDEs (finite-difference / finite-volume) on its own grid and time step.
2
Coupling via FRAME
Water fluxes (infiltration, recharge, baseflow, overbank) are exchanged at every synchronisation step.
3
Water-Balance Engine
A comprehensive utility tracks every storage change and flux for any sub-domain or the whole catchment.
4
Result Files
Time-series (dfs0), grid series (dfs2/dfs3) and flood maps are written; post-processing tools generate maps, hydrographs and statistics.
Typical Output Products
▸ River discharge & stage hydrographs
▸ Groundwater head maps & time series
▸ Soil moisture profiles & maps
▸ Actual ET and recharge grids
▸ Overland water depth & flood extent
▸ Detailed catchment water balances
▸ Flow vectors and velocity fields
▸ Nutrient / contaminant concentrations (with AD module)

## Slide 7
RESEARCH APPLICATIONS
07
7 / 9
Fields of Use in Academic Work
Catchment Hydrology & Yield
Water-balance studies, runoff generation mechanisms, sustainable yield assessment.
Climate-Change Impact
Scenario modelling of altered precipitation, temperature and extreme events on water resources.
Flood & Drought Risk
Distributed flood inundation, drought vulnerability and early-warning system development.
Surface–Groundwater Interaction
Quantifying baseflow, bank storage and conjunctive-use management.
Contaminant Fate & Transport
Advection–dispersion of solutes, nutrient leaching and remediation design (with AD/GC modules).
Ecological Restoration
Peatland rewetting, wetland hydrology, habitat response to hydrological change.

## Slide 8
RESEARCH APPLICATIONS
08
8 / 9
Further Academic & Applied Domains
Irrigation scheme optimisation & crop-water modelling
Mine-water management and dewatering assessment
Environmental Impact Assessments (EIAs)
Eutrophication mitigation & nutrient budgets
Green infrastructure / nature-based solutions
Land-use change impact studies
Water-protection-zone vulnerability mapping
Integrated Water Resources Management (IWRM)
Why researchers choose MIKE SHE
Ability to represent complex surface–subsurface feedbacks at catchment scale • Flexible process complexity • Seamless coupling with MIKE 1D / MIKE+ • Rich spatial and temporal outputs • Strong water-balance diagnostics • Decades of peer-reviewed application worldwide

## Slide 9
KEY TAKEAWAYS
MIKE SHE in one slide
01
Fully integrated, physically-based model of the complete land-phase water cycle.
02
Six core modules (ET, OC, UZ, SZ, SM, EX) dynamically coupled via FRAME.
03
Inputs span climate, topography, soils, geology, vegetation and river geometry.
04
Outputs include hydrographs, heads, soil moisture, ET, recharge and detailed water balances.
05
Widely applied in academic research on climate impacts, floods, droughts, ecology and contaminant transport.